## Slide 1: fNIRS data analysis
Baralt, Darcy-Mahaney, Jung et al.
06/20/2019

## Slide 2: Go-NoGo tasks for both Adults and Kids

## Slide 3
Summary: hbO:The task activation patterns differed significantly across the language study groups and the age cohorts. The hbO levels are significantly higher in response to No-Go task in the heritage group when compared to the monolingual group. However, in the bilingual group, the hbO levels are significantly lower in response to No-Go task. Out of 22 fNIRS channels, made up of source/detector pair, the number of channels that have shown significantly higher hbO levels is 1, 9, and 2 for bilingual, heritage and monolingual group respectively. In the bilingual group, three channels show significantly lower hbO levels.
In contrast, in children cohort, both the bilingual and monolingual group showed a significant decrease in hbO levels. In the bilingual children group, five channels showed a significant decrease in hbO levels when compared to two channels in the monolingual children study group.
In adults, the Brodmann area (10L) of the brain that is related to memory encoding and retrieval and use of language (generating sentences, word-stem completion, verbal fluency, and syntactic processing) showed a significant increase in hbO levels in both heritage and monolingual groups. Whereas, in the bilingual group, the hbO levels are significantly decreased. Also, the heritage group showed significantly higher levels of the hbO levels in the Brodmann area (46R) that involves in “working memory, sustaining attention, and regulating self-control”. Parts of the brain (Brodmann area 8L, 8R, and 9L) that are involved with “motor planning, organization, regulation and management of uncertainty” are also showed a significant increase in hbO levels. [need to be cautious in over interpreting this section]
[The mapping of the channels to Brodmann areas are done for Adults and not for children. We need to be extremely cautious in interpreting the results]
In children, the Brodmann area (10R) of the brain that is related to memory encoding and retrieval and use of language (generating sentences, word-stem completion, verbal fluency, and syntactic processing) and the Brodmann area (9L) that involves in “motor planning and organization” showed a significant decrease in hbO levels in bilingual group. Whereas, in the monolingual group, the hbO levels are significantly decreased in the parts of the brain (Brodmann area 8L and 9R) that are involved with “motor planning, organization, regulation and management of uncertainty”.
See additional figures at the end of the main slide deck

## Slide 4: Task activation brain areas at group level – (NG-Go) – hbR
Statistical contrast heat maps for change in cerebral de-oxyhemoglobin concentration (hbR) levels contrasting inhibitory executive functional (No-Go) task vs. control (Go) task. Column A represent the data from Adults cohort and Column B from Children cohort. Rows C-D represent data from bilingual, heritage and monolingual study groups. Red filled circles ( ) on the 10-20 EEG montage indicate NIRS light source and blue filled circles ( ) indicate NIRS light detector. Red (t statistic >0) indicates increased concentration levels and blue (t statistic < 0) indicates decreased concentration levels.
The task activation patterns differ significantly across the language study groups and the age cohorts. The hbR levels are significantly higher in response to No-Go task in the monolingual group when compared to the heritage group. However, in the bilingual group, the hbR levels are not significantly changed in response to No-Go task. In contrast, in children cohort, the monolingual showed significant increase in hbR levels while bilingual group showed a significant decrease in hbR levels.
B: Children
A: Adults
Bilingual
Heritage
Monolingual
C
D
E

## Slide 5
Summary: hbR:
The task activation patterns differ significantly across the language study groups and the age cohorts. The hbR levels are significantly higher in response to No-Go task in the monolingual group when compared to the heritage group. However, in the bilingual group, the hbR levels are not significantly changed in response to No-Go task. Out of 22 fNIRS channels, made up of source/detector pair, the number of channels that have shown significantly higher hbR levels is 2 and 3 for heritage and monolingual group respectively.
In contrast, in children cohort, the monolingual showed significant increase in hbR levels while bilingual group showed a significant decrease in hbR levels.
In the bilingual children group, two channels showed a significant decrease in hbR levels and in the monolingual group four channels showed a significant increase in hbR.
In adults, there is no significant changes in hbR levels in the bilingual group. While in both the heritage and monolingual groups showed significantly higher levels of the hbR levels in the Brodmann area (46R/L) that involves in “working memory, sustaining attention, and regulating self-control”. Also in the heritage group, parts of the brain (Brodmann area 9R, and 10L) that are involved with “memory encoding and retrieval and use of language, motor planning, organization, regulation and management of uncertainty” are also showed a significant increase in hbR levels. [need to be cautious in over interpreting this section]
[The mapping of the channels to Brodmann areas are done for Adults and not for children. We need to be extremely cautious in interpreting the results]
In children, in the monolingual group, the hbR levels are significantly increased in the parts of the brain (Brodmann area 9R, 10L and 46R). While in bilingual group, the hbR levels are significantly decreased in the parts of the brain (Brodmann area 8R and 9L).

## Slide 6: DCCS tasks for both Adults and Kids

## Slide 7: Task activation brain areas at group level – DCCS (Shape)– hbO
Kids
Adults
Bi-lingual
Heritage
Mono-lingual
A
B
C
D
E
F

## Slide 8: Task activation brain areas at group level – DCCS (Color)– hbO
Kids
Adults
Bi-lingual
Heritage
Mono-lingual
A
B
C
D
E
F

## Slide 9: Task activation brain areas at group level – DCCS (Border)– hbO
Kids
Adults
Bi-lingual
Heritage
Mono-lingual
A
B
C
D
E
F

## Slide 10: Task activation brain areas at group level – DCCS (Shape)– hbR
Kids
Adults
Bi-lingual
Heritage
Mono-lingual
A
B
C
D
E
F

## Slide 11: Task activation brain areas at group level – DCCS (Color)– hbR
Kids
Adults
Bi-lingual
Heritage
Mono-lingual
A
B
C
D
E
F

## Slide 12: Task activation brain areas at group level – DCCS (Border)– hbR
Kids
Adults
Bi-lingual
Heritage
Mono-lingual
A
B
C
D
E
F
Task activation (NG - GO) [read as NoGo minus Go] for Bilingual (hbO (A) and hbR (D), heritage (hbO (B) and hbR (E), monolingual (hbO (C) and hbR (F)) groups.
Brain activation areas for each group that are statistically significant are shown. Red indicates increased activation and blue indicates decreased activation.
Note: Task activation results can be projected on to brain atlas (tried and needed some troubleshooting )

## Slide 13: fNIRS data analysis pipeline
Using the analysis process based on the following paper. Fishburn, F. A., Hlutkowsky, C. O., Bemis, L. M., Huppert, T. J., Wakschlag, L. S., & Perlman, S. B. (2019). Irritability uniquely predicts prefrontal cortex activation during preschool inhibitory control among all temperament domains: A LASSO approach. Neuroimage, 184, 68-77. Retrieved from https://www.ncbi.nlm.nih.gov/pubmed/30213776. doi:10.1016/j.neuroimage.2018.09.023

## Slide 14
Read the raw data:
  Convert NIRx data format to Homer2 data format. Some of our data was collected with older version of the NIRStar data acquisition software. To work with NIRS Toolbox, the data needs to be converted to Homer2 data format first.
  Matlab code was modified to read in the events marked using the NIRSlab
Process the raw data:
  Trim the data (removing additional data before/after blocks).
  Convert voltage to optical density. Use the inbuilt routine to calculate unitless zero-mean log change of the data.
  Apply 4th-order butterworth band-pass filter which passes frequencies between 0.01 and 0.5 Hz
    Physiological noise in fNIRS
      Slow motion (< 0.01 Hz)
      Changes in blood pressure, vasoreactivity, CO2 concentration, and the autonomic nervous system fluctuations ( 0.01–0.2 Hz) – could still affect our results
      Respiration ( 0.2–0.6 Hz ) – could still affect our results
      Cardiac (0.6–2.5 Hz)
  Converting optical density to hbO and hbR using modified Beer’s Lambert Law (Ref: Jacques, Steven L. "Optical properties of biological tissues: a review." Physics in medicine and biology 58.11 (2013): R37) with partial pathlength factor (PPF) = 5 / 50;
    Takes into account age of subject (need to implement) [Ref:Scholkmann, F., & Wolf, M. (2013). General equation for the differential pathlength factor of the frontal human head depending on wavelength and age. J Biomed Opt, 18(10), 105004. Retrieved from https://www.ncbi.nlm.nih.gov/pubmed/24121731. doi:10.1117/1.JBO.18.10.105004]

## Slide 15
  Apply “Temporal Derivative Distribution Repair (TDDR)” filter to correct motion artifacts by downweighting outlier fluctuations. (Ref : Fishburn, Frank A., Ludlum, Ruth S., Vaidya, Chandan J., and Medvedev, Andrei V. "Temporal Derivative Distribution Repair (TDDR): A motion correction method for fNIRS." NeuroImage 184 (2019): 171-179.)
    Should try to implement other noise removal options for discussion sake or write a statement in the paper citing this paper that refers to different outcomes with different noise removal techniques (Ref: Hocke, L., Oni, I., Duszynski, C., Corrigan, A., Frederick, B., & Dunn, J. (2018). Automated Processing of fNIRS Data—A Visual Guide to the Pitfalls and Consequences. Algorithms, 11(5), 67. doi:10.3390/a11050067)
  To quickly view the data integrity across all the subjects, a matlab routine was developed.
Subject level stats using General Linear Model (GLM)
  Coefficients were estimated using autoregressive iteratively-reweighted least square approach and 3rd-order Legendre polynomial repressor to account for slow drift (Ref: Barker, Jeffrey W., Ardalan Aarabi, and Theodore J. Huppert. "Autoregressive model based algorithm for correcting motion and serially correlated errors in fNIRS." Biomedical optics express 4.8 (2013): 1366-1379.)
    Other options to be explored for the discussion purposes and to make sure we are making very bold claims. This paper refers to the difference in statistical differences for different procedures (Ref: Pfeifer, M. D., Scholkmann, F., & Labruyère, R. (2018). Signal Processing in Functional Near-Infrared Spectroscopy (fNIRS): Methodological Differences Lead to Different Statistical Results. Frontiers in Human Neuroscience, 11. doi:10.3389/fnhum.2017.00641 )
    Other options in nirs toolbox are OLS, NIRS-SPM, MV-GLM, non linear GLM
  Basic canonical HRF model: hemodynamic response model (duration: task time (24 for Go/NoGo and 20 for DCCS )) [other types of hrf can also be used]
  Subject level contrasts

## Slide 16
Mixed Effects
  Linear mixed-effects model fit by maximum likelihood method; isotropic covariance pattern;
  Effect of condition for each group, controlling for subject on hbO and hbR concentration levels (Baseline, Go, No-Go, Control, Border, Color and Shape) across subjects within each group (ML, HS, BL)
  Contrasts NoGo vs. Go; Border vs Control; Shape vs Control ; Color vs Control
  Using the full covariance noise model to control for the interdependence of measurements (e.g., artifacts or physiology that share noise across multiple channels).

## Slide 17
fNIRS collectively measure both hemodynamic and metabolic responses to evoked neuronal activity + physiological noise + external noise + instrument noise
Hemodynamic response evoked by neuronal activity
Increase cerebral blood flow and cerebral blood volume
  Increase hbO (higher signal change)
  Decrease hbR (lower signal change compared to hbO)
Metabolic response evoked by neuronal activity
Increases neuronal oxygen metabolism
  Decrease hbO (lowest signal change)
  Increase hbR (lowest signal change)

## Slide 18: Additional figures for Go-NoGo

## Slide 19: Task activation brain areas at group level – (NG-Go) – hbO
B: Children
A: Adults
Bi-lingual
Heritage
Mono-lingual
C
D
E
Only the channels that showed statistically significant change in activation patterns are shown.

## Slide 20: Task activation brain areas at group level – (NG-Go) – hbR
B: Children
A: Adults
Bi-lingual
Heritage
Mono-lingual
C
D
E
Only the channels that showed statistically significant change in activation patterns are shown.

## Slide 21
22 channel data view mapped to Brodmann areas. Red increased concentration levels; Blue reduced concentration levels

## Slide 22
22 channel data view mapped to Brodmann areas. Showing only channels that are increased concentration levels.
Ignore (p<1) in the figure

## Slide 23
22 channel data view mapped to Brodmann areas. Showing only channels that are decreased concentration levels.
Ignore (p<-1) in the figure

## Slide 24
22 channel data view mapped to Brodmann areas. Red increased concentration levels; Blue reduced concentration levels

## Slide 25
22 channel data view mapped to Brodmann areas. Showing only channels that are increased concentration levels.
Ignore (p<1) in the figure

## Slide 26
22 channel data view mapped to Brodmann areas. Showing only channels that are decreased concentration levels.
Ignore (p<-1) in the figure

## Slide 27: Brodmann Areas –fNirs mapping
EEG Electrode | fNIRS Channel | Brodmann Area | Area Involved In
FP1, AFp1, FPz | 4, 7, 12 | 10L | Executive function
 |  |  | Memory encoding and retrieval
Fp2, AFp2 | 14, 13 | 10R | Use of language (generating sentences, word-stem completion, verbal fluency, and syntactic processing)
AF7 | 3 | 46L | Working memory
 |  |  | Sustaining attention
AF8, F6 | 21, 22 | 46R | 
 |  |  | Regulating self control
AF3, Afz | 5, 8, 10 | 9L | Motor planning
 |  |  | Organization
Afz, AF4 | 17, 15 | 9R | 
 |  |  | Regulation
F4, F2, AFF2 | 20, 11, 16 | 8R | Management of uncertainty
Fz, F1, F3 | 9, 2, 1 | 8L | Control of eye movement

## Slide 28: Additional figures for DCCS